## Slide 1: Spectre vulnerability

## Slide 2
History

## Slide 3
1 June 2017. That was the moment when
really knew they messed up

## Slide 4
Discovered by Jann Horn from Google’s Project Zero. It was presented on 1 June 2017 to the affected hardware vendors and on 3 January 2018 was made public.
It started a wave of speculative execution research. Many CVEs regarding this vulnerability exist, making Spectre a class of attacks.
Due to its nature, this vulnerability is not programming language dependent.

## Slide 5
Recipe for disaster

## Slide 6
1. Ingredients:

## Slide 7
The anatomy of a CPU
The CPU is the “brainz” of the computer.
Just as the brain has different zones responsible for executing different functions, so too does the CPU.
Control Unit
(CU)
Arithmetic &
Logic Unit
(ALU)
Memory
Management
Unit (MMU)
Pointer to
instruction
Output
Registers

## Slide 8
Instruction processing efficiency
The CU is responsible for decoding the opcode (instruction bytes op = operation, code = code) and to program the ALU.
The ALU is the place where the computation actually takes place.
Both CU, ALU and other components operate based on a clock cycle. Meaning each component does work once a clock cycle. (For a 2 GHz processor, each component does work each seconds).
The ALU can take more than 1 clock cycle to process an instruction
The number of instructions a processor does per cycle is called IPC
(Instructions Per Cycle)
CU
ALU
Opcode
Result
A number
of clock cycles

## Slide 9
SPEEEED!
In order to improve the IPC, manufacturers started adding more ALUs in a CPU, creating what is called an instruction pipeline.
Each clock cycle the instruction passes lower in the pipeline, allowing another one to start processing.
This mechanism greatly improves the IPC, making it almost unitary.
CU
ALU
ALU
ALU
Instruction N
Instruction N - 1
Instruction N - 2
Instruction N - 3
Instruction N - 4
Output N - 5

## Slide 10
MORE SPEEEED!
To increase IPC over the value of 1, multiple instruction pipelines can reside into a single CPU (core). This enables parallel instruction execution.
Dependent instructions cannot be parallel pipelined, this is the reason why compilers reorder instructions internally and why (probably) you cannot write faster code in assembly.
A problem arises: how to parallel pipeline instructions when an execution transfer instruction is encountered?
CU
ALU
ALU
Instruction N - 1
Instruction N - 3
Instruction N - 5
CU
ALU
ALU
Instruction N - 2
Instruction N - 4
Instruction N - 6
Output N - 7
Output N - 8

## Slide 11
JUMP!
In order to maintain instruction pipelining, a mechanism called speculative branch execution was introduced.
It predicts if an conditional control transfer execution instruction (conditional jump) will be taken or not.
Latest processor models use a hardware implemented perceptron as a speculative branch predictor.
Based on the predicted branch, instructions are pipelined. If the prediction was incorrect (deduced when all necessary instructions have finished pipelining ), the pipelined results are discarded and the pipeline starts again on the correct branch.
Usually, the pipelining should stop and await processing of the results to decide the outcome of a conditional jump.
To jump or
not to jump?
Continue pipelining here
To jump or
not to jump?
Discard & start again here :(
Correct
prediction
Incorrect
prediction
Hopefully shouldn’t have jumped here
jump
Don’t jump

## Slide 12
Cache
If the CPU tries to access a memory area that is not cached (known as cache miss) that area is then fetched and stored into cache.
Cache memory is a small, fast memory area close to the CPU where frequently used data are stored from the slower but larger RAM memory.
$
This mechanism works the same for speculative execution but when a missprediction occurs, the cache is not cleared. (The accessed data from memory will still reside in cache even after the CPU deduced that the pipelined branch was not right)
CPU
Cache
RAM
Hey, got this mem?
Nope, let me ask RAM
There you go, also you might
wanna store that
*stores mem*
There you go
Cached memory is much faster accessed than RAM memory

## Slide 13
2. Recipe:

## Slide 14
Spectre Attack
Using the previous information a hacker can “bake” a code that enables him to read protected memory.
Phase 1: Train the branch predictor to perform a code.
Data = [1,2,3,4]
X = 0
If( X < Data.length ) {
Secret = Data[X]
}
If( X < Data.length ) {
Secret = Data[X]
}
……………………………
The code is seemingly harmless, just reads a value from an array
It is executed a number of times in which the branch predictor deduces that the if condition is true and the code within the if has a good chance to be the correct one to be executed

## Slide 15
Phase 2: Force the processor to read and cache protected memory.
……………
X = 10000
If( X < Data.length ) {
Secret = Data[X]
}
The now trained predictor will execute the if with the new X value. The protected memory will be cached into memory.
Even when the predictor realizes that the branch shouldn’t have been executed, the memory cannot be erased from cache.

## Slide 16
Phase 3: Retrieve the cached secret.
…..
Letters = [“a”, “b”, …, “z”]
// Get a memory access time baseline
time_start = timenow()
char f = Letters[secret]
time_end = timenow()
print(“baseline delta = ” + time_end – time_start)
For(int i=0; i < Letters.len; i++)
{
// Cache a possible value for secret
char c = Letters[i]
// If the time has dropped, we have fund the secret value
time_start = timenow()
char f = Letters[secret]
time_end = timenow()
print(“delta = ” + time_end – time_start)
}
To deduce the cached value we first must:
Time the memory access for secret as a baseline.
Cache a value that might be a value for our secret
Time a new memory access for the secret
If the access time dropped considerably => We have found the protected memory value
If the access time did not drop, try another value and continue steps 2 and 3

## Slide 17
3. Impact & Consequences:

## Slide 18
As of 2018 almost all computational devices are affected by Spectre (desktops, laptops, mobile devices).
Due to its nature Spectre is a specific vulnerability and can be hard to exploit, reducing its risc.
Spectre might have a real impact on cloud platform providers, as it has the potential to force a hypervisor to dump guest information.
No known attacks in the wild.

## Slide 19
4. Real world examples:

## Slide 20
A known POC for the Spectre attack was the dumping of browser data using JavaScript. Proposed by Microsoft vulnerability researchers, it used a simple JavaScript code that performed the same steps described previously (train the branch predictor, force the processor into caching a protected value and dumping the cached value).
Since JavaScript doesn’t offer access to some useful low level instructions (such as clflush) other approaches were taken.
The POC was successful.
Chrome, Firefox, Tor and other browsers implemented as a mitigation restrains on the resolution of browser timers. As a result, it is harder to determine if a value was indeed cached or not.

## Slide 21
5. Mitigations:

## Slide 22
No single patch can be created to cover the whole Spectre class of attacks.
At hardware level, Intel tests selective TLB flushing to mitigate the Spectre vulnerability. At this time new CPU instruction eliminating branch speculation have been introduced such as LFECNCE
Operating systems and firmware providers have implemented specific patches in order to prevent some forms of Spectre attacks.
Applications such as browser implement some mitigations, such as restrains on the resolution of timers, in order to avoid these attacks.
Because the problem of Spectre is deeply rooted in the CPU architecture and greatly improves the processing speed, the speculative execution mechanism cannot be removed.